## Slide 1
Intro to the University of Iowa Utility Data System
University of Iowa Data Science Organization
October 26, 2023

## Slide 3: Building Utilities
Electricity: Uses electricity from the UIowa electric grid
Steam: Heats the building with steam from the UIowa steam system
Chilled Water: Cools the building with chilled water from the UIowa chilled water system
Potable Water: Serves drinking water from the UIowa water system
Schaeffer Hall
Utilities

## Slide 4: Utility Billing
The UIowa utility system bills buildings for their energy and water usage similar to a regular utility company

## Slide 5: Utility Billing

## Slide 6: Steam Generation
The power plant houses 5 boilers to produce steam. 3 burn natural gas and 2 burn energy pellets (pre-consumer papers and plastics)
The system can also generate steam from two remote boilers: one located in the hospital and the other on the west side of campus. Both remote boilers burn natural gas.

## Slide 7: Steam Distribution Grid
The system distributes steam across campus at two pressures: 150 PSI and 20 PSI

## Slide 8: Electric Generation
The power plant houses 3 steam turbines and 4 natural gas generators to produce electricity.
The utility system also purchases electricity from MidAmerican Energy Company.
System has two solar arrays in the Renewable Energy Discovery District.

## Slide 9: Electric Distribution Grid

## Slide 10: Power Plant Overview

## Slide 11: Chilled Water Generation
3 chilled water plants housing 16

## Slide 12
Northwest Plant
Power Distribution West
Power Distribution East
Chilled Water Distribution
West
Substation U
161 kV
Substation L
69 kV
Across Campus Tie (N/O)
West Chiller Plant
North Chiller Plant
Chilled Water Distribution East
University of Iowa Main Campus Utilities
UIHC
East Campus
West Campus
Steam Chillers (3)
Electric Chillers (8)
Steam Chiller (1)
Steam Chillers (3)
Electric Chillers (1)
Legend: Electrical Chilled Water
Steam Potable Water
8
10
11
Solid Fuel Boilers
Natural Gas Boilers
Steam Turbine Electric Generators
Steam Distribution West
Steam Distribution East
Water Treatment Plant
Potable Water Distribution
East
Potable Water Distribution
West
7
Main Power Plant
NG
Boilers
WCB
Natural Gas Engine Electric Generators
12
NGB

## Slide 13: Data/Coding Exercise
Exercise: Get the hourly energy usage of Schaeffer Hall over the past 5 (or so) years.
Important Notes:
Power | Energy
Kilowatts (kilojoules per seconds) | Kilowatt-hours (3600 kilojoules)
MMBTUs per hour | Metric Million British Thermal Unit (MMBTU)
MMBTUs per hour | Metric Million British Thermal Unit (MMBTU)
Energy is served in three forms: electric, steam, and chilled water
Data is recorded in units of power (a unit of energy over a unit of time)
Discoveries to make:
What day/hour was the highest energy usage for each resource
What day/hour was the highest total energy usage (all resources combined)
?

## Slide 14: UIowa Hackathon Solar Performance Challenge

## Slide 16: Modeling Layer
f
f
f
f
f
f
f
f
f
f
f
f
f
f
f
f
f
f
f
f

## Slide 17: No Coal by 2025
Fuel Comparison
Coal
Energy Pellets
1.02 Kg-CO2 per pound burned
10,940 BTUs per pound
$0.041 per pound
Details: Bituminous
0.61 Kg-CO2 per pound burned
9,529 BTUs per pound
$0.048 per pound
Details: %57.5 Biomass, %42.5 Pre-Consumer Plastics

## Slide 18
Replacing Coal with Energy Pellets
18,220 Metric Tons of CO2 Prevented! (%12.5 decrease)

## Slide 19
Replacing Coal with Energy Pellets
$827,549 more in Fuel Costs (4.4 percent increase)

## Slide 20: Questions and Contacts
Ryan Policheri, Senior Software Developer: ryan.policheri@engie.com
Wylan Gao, Energy Data Center Intern: wylan.gao@engie.com
Questions?
Contacts: